## Slide 1: CS 31006: Computer Networks – Transport Layer Services

## Slide 2: Protocol Stack Implementation in a Host
Software, Kernel
Firmware, Device Driver
Hardware
Physical
Data Link
Network
Transport
Application

## Slide 3: How Application Data Passes Through Different Layers
Physical
Data Link
Network
Transport
Application
HTTP Data
HTTP Header
Transport Layer Data
TCP Header
Network Layer Data
IP Header
Data Link Layer Data
MAC Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
PHY Header
PHY Trailer

## Slide 4: Transport Layer Services
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Transport
Data Link
Datagram delivery (unreliable)
Network

## Slide 5: Connection Establishment
This is a simple primitive for connection establishment – but does this work good?
Client
Server
LISTEN
CONNECT
CONNECTION REQ
CONNECTION ACK

## Slide 6: Connection Establishment
Consider a scenario when the network can lose, delay, corrupt and duplicate packets (the underline network layer uses unreliable data delivery)
Consider retransmission for ensuring reliability – every packet uses different paths to reach the destination
Packets may be delayed and got struck in the network congestion, after the timeout, the sender assumes that the packets have been dropped, and retransmits the packets

## Slide 7: Connection Establishment
How will the server differentiate whether CONNECTION REQ-1 is a new connection request or a duplicate of the CONNECTION REQ-2?
Client
Server
LISTEN
CONNECT
CONNECTION REQ - 1
CONNECTION REQ - 2
It may happen that the server has crashed and reinitiated the connection. So distinguishing between these two is essential

## Slide 8: Connection Establishment
Protocol correctness versus Protocol performance – an eternal debate in computer networks …
Delayed duplicates create a huge confusion in the packet switching network. A major challenge in packet switching network is to develop correct or at least acceptable protocols for handling delayed duplicates

## Slide 9: Connection Establishment – Handling Delayed Duplicates
Solution 1: Use Throwaway Transport Address (Port Numbers)
  Do not use a port number if it has been used once already – Delayed duplicate packets will never find their way to a transport process
  Is this solution feasible?
Solution 2: Give each connection a unique identifier chosen by the initiating party and put in each segment
  Can you see any problem in this approach?

## Slide 10: Connection Establishment – Handling Delayed Duplicates
Solution 3: Devise a mechanism to kill off aged packets that are still hobbling about (Restrict the packet lifetime) – Makes it possible to design a feasible solution
Three ways to restrict packet lifetime
  Restricted Network Design – Prevents packets from looping (bound the maximum delay including congestion)
  Putting a hop count in each packet – initialize to a maximum value and decrement each time the packet traverses a single hop (most feasible implementation)
  Timestamping each packet – define the lifetime of a packet in the network, need time synchronization across each router.
Design Challenge: We need to guarantee not only that a packet is dead, but also that all acknowledgements to it are also dead

## Slide 11: Connection Establishment – Handling Delayed Duplicates
Let us define a maximum packet lifetime T – If we wait a time T secs after a packet has been sent, we can be sure that all traces of it (packet and its acknowledgement) are now gone
Rather than a physical clock (clock synchronization in the Internet is difficult to achieve), let us use a virtual clock – sequence number generated based on the clock ticks
Label segments with sequence numbers that will not be reused within T secs.
The period T and the rate of packets per second determine the size of the sequence number – at most one packet with a given sequence number may be outstanding at any given time

## Slide 12: Sequence Number Adjustment
Two important requirements (Tomlinson 1975, Selecting Sequence Numbers)
  Sequence numbers must be chosen such that a particular sequence number never refers to more than one byte (for byte sequence numbers) at any one time (how to choose the initial sequence number)
  The valid range of sequence numbers must be positively synchronized between the sender and the receiver, whenever a connection is used (three way handshaking followed by the flow control mechanism – once connection is established, only send the data with expected sequence numbers)

## Slide 13: Why Initial Sequence Number is Important
A Delayed duplicate packet of connection 1 can create a confusion for connection 2
Packet Lifetime T
Time
Sequence Numbers
Connection 1
Connection 2
Conn 1 crashed
Conn 2 initialized

## Slide 14: What We Ideally Want? Or …
Packet Lifetime T
Time
Sequence Numbers
Connection 1
Connection 2
Conn 1 crashed
Conn 2 initialized

## Slide 15: What We Ideally Want? Either …
Packet Lifetime T
Time
Sequence Numbers
Connection 1
Connection 2
Conn 1 crashed
Conn 2 initialized

## Slide 16: Connection Establishment – Handling Delayed Duplicates
If a receiver receives two segments having the same sequence number within a duration T, then one packet must be the duplicate. The receiver then discards the duplicate packets.
For a crashed device, the transport entity remains idle for a duration T after recovery, to ensure that all packets from the previous connection are dead – not a good solution
Adjust the initial sequence numbers properly - A host does not restart with a sequence number in the forbidden region, based on the sequence number it used before crash and the time duration T.

## Slide 17: How do We Ensure that Packet Sequence Numbers are Out of the Forbidden Region
Two possible source of problems
  A host sends too much data too fast on a newly opened connection
  The data rate is too slow that the sequence number for a previous connection enters the forbidden region for the next connection
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 18: Adjusting the Sending Rate based on Sequence Numbers
The maximum data rate on any connection is one segment per clock tick
  Clock ticks (inter-packet transmission duration) is adjusted based on the sequences acknowledged – ensure that no two packets are there in the network with same sequence number
  We call this mechanism as self-clocking (used in TCP)
  Ensures that the sequence numbers do not warp around too quickly (RFC 1323)
We do not remember sequence number at the receiver: Use a three way handshake to ensure that the connection request is not a repetition of an old connection request
  The individual peers validate their own sequence number by looking at the acknowledgement (ACK)
  Positive synchronization among the sender and the receiver

## Slide 19: Three Way Handshake
By looking at the ACK, Host 1 ensures that Sequence number x does not belong to the forbidden region of any previously established connection
By looking at the ACK in DATA, Host 2 ensures that sequence number y does not belong to the forbidden region of any previously established connection
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 20: Three Way Handshake – CONNECTION REQUEST is a Delayed Duplicate
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 21: Three Way Handshake – CONNECTION REQUEST and ACKNOWLEDGEMENT both are Delayed Duplicates
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 22: Connection Release – Asymmetric Release
When one party hangs up, the connection is broken
This may results in data loss
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 23: Connection Release – Symmetric Release
Treats the connection as two separate unidirectional connections and requires each one to be released separately
Does the job when each process has a fixed amount of data to send and clearly knows when it has sent it.
What can be a protocol for this?
  Host 1: “I am done”
  Host 2: ”I am done too”
Does this protocol work good always?

## Slide 24: The Two Army Problem
No protocol exists to solve this
Let every party take independent decisions
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 25: Connection Release
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 26: Connection Release – Final ACK Lost
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 27: Connection Release – Response Lost
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 28: Connection Release – Response Lost and Subsequent DRs Lost
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 29: Ensure Reliability at the Transport Layer
Source: Computer Networks, Kurose, Ross

## Slide 30: Error Control and Flow Control
These features are used in both Data Link Layer and Transport Layer – Why?
Flow control and error control at the transport layer is essential
Flow control and error control at the data link layer improves performance

## Slide 31: Flow Control Algorithms
Stop and Wait Flow Control (Error Free Channel):

## Slide 32: Flow Control Algorithms
Stop and Wait (Noisy Channel):
Use sequence numbers to individually identify each frame and the corresponding acknowledgement
What can be a maximum size of the sequence number in Stop and Wait?
Automatic Repeat Request (ARQ)

## Slide 33: Stop and Wait ARQ – Sender Implementation
Source: Computer Networks, Kurose, Ross

## Slide 34: Problem with Stop and Wait
Every packet needs to wait for the acknowledgement of the previous packet.
For bidirectional connections – use two instances of the stop and wait protocol at both directions – further waste of resources
A possible solution: Piggyback data and acknowledgement from both the directions
Reduce resource waste based on sliding window protocols (a pipelined protocol)

## Slide 35: Stop and Wait versus Sliding Window (Pipelined)
Source: Computer Networks, Kurose, Ross

## Slide 36: Sliding Window Protocols
Each outbound segment contains a sequence number – from 0 to some maximum (2n-1 for a n bit sequence number)
The sender maintains a set of sequence numbers corresponding to frames it is permitted to send (sending window)
The receiver maintains a set of frames it is permitted to accept (receiving window)

## Slide 37: Sliding Window Protocols – Sending Window and Receiving Window
Source: http://ironbark.xtelco.com.au/subjects/DC/lectures/13/

## Slide 38: Sliding Window for a 3 bit Sequence Number
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 39: Sliding Window Protocols in Noisy Channels
A timeout occurs if a segment (or the acknowledgment) gets lost
How does the flow and error control protocol handle a timeout?
Go Back N ARQ: If segment N is lost, all the segments from segment 0 (start of the sliding window) to segment N are retransmitted
Selective Repeat (SR) ARQ: Only the lost packets are selectively retransmitted
  Negative Acknowledgement (NAK) or Selective Acknowledgements (SACK): Informs the sender about which packets need to be retransmitted (not received by the receiver)

## Slide 40: Go Back N ARQ – Sender Window Control
Source: Computer Networks, Kurose, Ross

## Slide 41: Go Back N ARQ
Source https://www.tutorialspoint.com/data_communication_computer_network/data_link_control_and_protocols.htm

## Slide 42: Go Back N ARQ – Sender
Source: Computer Networks, Kurose, Ross

## Slide 43: Go Back N ARQ – Receiver
Source: Computer Networks, Kurose, Ross

## Slide 44: Go Back N ARQ – A Bound on Window Size
Outstanding Frames – Frames that have been transmitted, but not yet acknowledged
Maximum Sequence Number (MAX_SEQ): MAX_SEQ+1 distinct sequence numbers are there
  0,1,…,MAX_SEQ
Maximum Number of Outstanding Frames (=Window Size): MAX_SEQ
Example: Sequence Numbers (0,1,2,…,7) – 3 bit sequence numbers, number of outstanding frames = 7 (Not 8)

## Slide 45: Go Back N ARQ – A Bound on Window Size
Let MAX_SEQ = 3, Window Size = 4
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
Timeout

## Slide 46: Go Back N ARQ – A Bound on Window Size
Let MAX_SEQ = 3, Window Size = 3
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
0
Timeout
Discards the wrong frame correctly

## Slide 47: Selective Repeat (SR) – Window Control
Source: Computer Networks, Kurose, Ross

## Slide 48: Selective Repeat ARQ

## Slide 49: Selective Repeat – A Bound on Window Size
Maximum Sequence Number (MAX_SEQ): MAX_SEQ+1 distinct sequence numbers are there
  0,1,…,MAX_SEQ
Maximum Number of Outstanding Frames ( =Window Size ): (MAX_SEQ+1)/2
Example: Sequence Numbers (0,1,2,…,7) – 3 bit sequence numbers, number of outstanding frames (window size) = 4

## Slide 50: Selective Repeat – A Bound on Window Size
Let MAX_SEQ = 3, Window Size = 3 [(MAX_SEQ+1)/2+1]
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
0
Timeout
1
2
1
2
1
2
1
2

## Slide 51: Selective Repeat – A Bound on Window Size
Let MAX_SEQ = 3, Window Size = 2
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
2
3
0
0
1
0
Timeout
1
2
1
2
1
2
Discards the wrong frame correctly

## Slide 52: Bandwidth Delay Product
Bandwidth Delay Product (BDP) = Link Bandwidth x Link Delay – an important metric for flow control
Consider Bandwidth = 50 Kbps, one way transit time (delay) = 250 msec
  BDP 12.5 Kbit
  Assume 1000 bit segment size; BDP = 12.5 segments
Consider the event of a segment transmission and the corresponding ACK reception – this takes a round trip time (RTT) – twice the one way latency.
Maximum number of segments that can be outstanding during this duration = 12.5 x 2 = 25 segments

## Slide 53: Bandwidth Delay Product – Implication on Window Size
Maximum number of segments that can be outstanding within this duration = 25 + 1 (as the ACK is sent only when the first segment is received) = 26
  This gives the maximum link utilization – the link will always be busy in transmitting data segments
Let BD denotes the number of frames equivalent to the BDP, w is the maximum window size
So, w = 2BD + 1 gives the maximum link utilization – this is an important concept to decide the window size for a window based flow control mechanism

## Slide 54: Implication of BDP on Protocol Design Choice
Consider the link bandwidth = 1Mbps, Delay = 1ms
Consider a network, where segment size is 1 KB (1024 bytes)
Which protocol is better for flow control?
  (a) stop and wait,
  (b) Go back N,
  (c) Selective Repeat
BDP = 1 Mbps x 1ms = 1 Kb (1024 bits)
The segment size is eight times larger than the BDP -> the link can not hold an entire segment completely
Sliding window protocols do not improve performance
Stop and Wait is better – less complexity

## Slide 55: Application Transport Interfacing – Sender Side
APPLICATION
write(), send()
TportSend()
Send Data to IP
Transmission Rate Control
USER
KERNEL
Trigger Periodically
Function names are hypothetical

## Slide 56: Application Transport Interfacing – Sender Side
APPLICATION
write(), send()
TportSend()
Send Data to IP
Transmission Rate Control
USER
KERNEL
Trigger Periodically
Transport Buffer - Sender
Different connections are treated differently, so we need connection specific source buffering
write() call blocks the port until the complete data is written in the transport buffer
Function names are hypothetical

## Slide 57: Application Transport Interfacing – Receiver Side
APPLICATION
read(), recv()
CheckBuffer()
USER
KERNEL
Transport Buffer - Receiver
Interrupt
Data from IP
TportRecv()
read() call blocks the port until the data is received and the complete data is read from the transport buffer
Function names are hypothetical

## Slide 58: Application Transport Interfacing – Receiver Side (Alternate Implementation)
APPLICATION
read(), recv()
PollBuffer()
Data from IP
USER
KERNEL
Transport Buffer - Receiver
poll()
get()
TportRecv()
Function names are hypothetical

## Slide 59: Organizing Transport Buffer Pool
If most segments are nearly the same size, organize the buffer as a pool of identically sized buffers (one segment per buffer)
For variable segment size – chained fixed sized buffer (buffer size = maximum segment size)
Space would be wasted if segment sizes are widely varied
Small buffer size – multiple buffers to store a single segment – added complexity in implementation

## Slide 60: Organizing Transport Buffer Pool
Variable size buffers (b)
  Advantage: better memory utilization
  Disadvantage: Complicated implementation
Single large circular buffer for every connection (c)
  Good use of memory only when connections are heavily loaded
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 61: Dynamic Buffer Management for Window Based Flow Control
Sender and receiver needs to dynamically adjust buffer allocations
Based on the rate difference between the receive rate by the transport entity and the receive rate by the application, the available size of the receiver buffer changes
Sender should not send more data compared to receiver buffer space – dynamically adjust the window size based on availability of receiver buffer space
Free Space at Receiver Buffer
Segments awaiting at the buffer
Segments read by the application

## Slide 62: Dynamic Buffer Management for Window Based Flow Control
Receiver forwards available buffer space through ACK
Ensure that the ACKs are flowing in the network continously

## Slide 63: Congestion Control in the Network
Consider a centralized network scenario – how can you maintain optimal flow rates?
10
20
5
2
6
4
2
11
18
S
D
50
50
Apply Max Flow Min Cut Theorem !
But this is hard in a real network …

## Slide 64: Congestion Control in the Network
Changing Bandwidth Allocation over Time
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 65: Congestion Control in the Network
Flows enter and exit network dynamically – so applying an algorithm for congestion control is difficult
Congestion avoidance: Regulate the sending rate based on what the network can support
Sending Rate = minimum (network rate, Receiver rate)
Gradually increase the network rate and observe the effect on flow rates (packet loss)
Comes from flow control – receiver advertised window size for a sliding window flow control

## Slide 66: Network Congestion – Impact over Goodput and Delay
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 67: Congestion Control and Fairness
Ensure that the rate of all the flows in the network is controlled in a fair way
A bad congestion control algorithm may affect fairness - Some flows can get starved
Hard fairness in a decentralized network is difficult to implement
Max-Min Fairness: An allocation is max-min fair if the bandwidth given to one flow cannot be increased without decreasing the bandwidth given to another flow with an allocation.

## Slide 68: Max-Min Fairness – An Example
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 69: AIMD – Efficient and Fair Operating Point for Congestion Control
Additive Increase Multiplicative Decrease (AIMD) – Chiu and Jain (1989)
Let w(t) be the sending rate. a (a > 0) is the additive increase factor, and b (0<b<1) is the multiplicative decrease factor

## Slide 70: AIMD – Design Rationale (Two Flows Example)
AIAD – Oscillate across the efficiency line
MIMD – Oscillate across the efficiency line (different slope from AIAD)
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 71: AIMD – Design Rationale (Two Flows Example)
The path converges towards the optimal point
Used by TCP - Adjust the size of the sliding window to control the rates
Source: Computer Networks (5th Edition) by Tanenbaum, Wetherell

## Slide 72
Let us look TCP design details …