## Slide 1: CS 31006: Computer Networks – Moving From End-to-End To Per Hop

## Slide 2: What We Have Learnt So Far …
The design of current network architecture is based on experience and requirements
Physical
Physical
Data Link
Physical
Data Link
Network
Physical
Data Link
Network
Transport

## Slide 3: What We Have Learnt So Far …
Software, Kernel
Firmware, Device Driver
Hardware
Physical
Data Link
Network
Transport
Application
Protocol stack is implemented across different layers of the operating system

## Slide 4: What We Have Learnt So Far …
Physical
Data Link
Network
Transport
Application
HTTP Data
HTTP Header
Transport Layer Data
TCP Header
Network Layer Data
IP Header
Data Link Layer Data
MAC Header
HTTP Data
HTTP Header
TCP Header
IP Header
MAC Header
PHY Header
PHY Trailer
Each layer adds up its own information in the packet headers

## Slide 5: Every Layer Adds Up Their Own Services
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Transport
Data Link
Network
Addressing
Routing
Framing
Switching
Per Hop Flow Control
Access Control

## Slide 6: Transport Layer - Understand the Basic End-to-end Principles
Connection Establishment:
  Use sequence number selection principles to avoid delayed duplicates – differentiate new connections from old connections
Flow Control:
  Use sliding window principle to adjust flow rates based on what receiver can accept
Congestion Control:
  Use AIMD principles – ensure efficiency and fairness simultaneously without solving any complex mathematical optimization

## Slide 7: TCP Congestion Control – A Perfect Example of System Engineering
AIMD – support efficiency and fairness simultaneously

## Slide 8: TCP Congestion Control – A Perfect Example of System Engineering
Slow Start: Accelerate AIMD convergence

## Slide 9: TCP Congestion Control – A Perfect Example of System Engineering
Fast Retransmit: Use triple duplicate ACK to trigger a congestion (faster than timeout), retransmit the lost segment immediately and then apply slow start.
Fast Recovery: Do not apply slow start for thee DUPACKs (packets are still flowing in the network). For every DUPACK, transmit a segment starting from the lost segment. Once a new ACK is received, start AIMD instead of slow start.

## Slide 10: Network (Internet) Layer Services
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Transport
Data Link
Network
Addressing
Routing
Datagram delivery (unreliable)

## Slide 11: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
SW Lab 1
SW Lab 2
Router
CSE Network

## Slide 12: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
CSE Network
EEE Network
SW Lab 1
SW Lab 2
EE Lab 1
EE Lab 2
IITKGP Network

## Slide 13: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
IITKGP Network
IITBBS Network
EEE
CSE
EEE
CSE
ERNET Network

## Slide 14: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
BSNL Network
IITKGP
IITBBS
BSNL Public
BSNL Corporate
Bharti Airtel Network
ERNET Network

## Slide 15: Internet Architecture
Autonomous Systems (AS) – A set of LANs for an administrative domain, identified by a unique AS number, and the routing policies are controlled by a single administrator.
Local Area Network (LAN) – A set of devices with a common layer 3 gateway

## Slide 16: Autonomous System Graph for India
Source: https://labs.apnic.net/vizas/#IN

## Slide 17: Internet Architecture
Internet Service Providers (ISP) – An AS provides Internet connectivity to another group of ASes or end users

## Slide 18: Peering between ISPs

## Slide 19: Communication between Two Nodes over ISPs

## Slide 20: IP Addressing – Basic Principles
We need to forward data packets from one network to another network via different intermediate networks.
AS 10
AS 11
AS 13
AS 12
Host 1
Host 2

## Slide 21: IP Addressing – Basic Principles
The address should identify a network as well as a host inside a network
AS 10
AS 11
AS 13
AS 12
Host 1
Host 2

## Slide 22: IP Addressing
Divide the address space (32 bit in IPv4) among network address and host address
The old age – Classful addressing: Fixed number of bits for network address and host address
Network address
Host address

## Slide 23: Classful Addressing
How to identify a class – use the first few bits
  0 – Class A, 10 – Class B, 110 – Class C, 1110 – Class D, 1111 – Class E

## Slide 24: Network Address and Broadcast Address
Network address – identify a network
  All 0’s in the host address part
  Ex-1 (Class A): 01111110.00000000.00000000.00000000 (126.0.0.0)
  Ex-2 (Class B): 10111101.11101001.00000000.00000000 (189.233.0.0)
Broadcast address – send the data to all the hosts of a network
  All 1’s in the host address part
  Ex-1 (Class A): 01111110.11111111.11111111.11111111 (126.255.255.255)
  Ex-2 (Class B): 10111101.11101001.11111111.11111111 (189.233.255.255)
How many valid hosts can be there in a Class A, in a Class B and in a Class C IP address?

## Slide 25: Subnetting and Supernetting – Classless Inter-domain Routing (CIDR)
You have 255 hosts in a network. Which IPv4 address class will you use – Class C or Class B ?
  Class C – not possible
  Class B – huge address space is lost (using only 255 addresses out of possible 216-2 addresses)
Split a large network or combine multiple small networks for efficient use of address space
  Subnetting – divide a large network into multiple small networks
  Supernetting – combine multiple small networks into a single large network
Subnet mask – denote the number of bits in the network address field

## Slide 26: Divide a Network into Subnets

## Slide 27: CIDR – Addressing Format
Host Address
Subnet Address
We write the IP address as 191.180.83.235/12 in CIDR notation
  The first 12 bits are the network address and rest (32-12)=20 bits are for host address
The subnet mask is 255.240.0.0
10111111
10110100
01010011
11101011
11111111
11110000
00000000
00000000
IP Address
Netmask

## Slide 28: CIDR - Manual IP Setting in the OS

## Slide 29: Divide a Network into Subnets
Let the IP address of a network is 203.110.0.0/16
We want to divide this network into three subnets
We need 3 bits for subnets – why not 2 bits?
  Subnet 1 – 100, Subnet 2– 101, Subnet 3 – 110
Rest 13 bits are used for addressing the hosts of those subnets.
The subnets are – 203.110.128.0/19, 203.110.160.0/19, 203.110.192.0/19

## Slide 30: All Zero and All One Subnets
192.168.0.0/16
192.168.0.0/17
192.168.128.0/17
192.168.0XXXXXXX.X
192.168.1XXXXXXX.X
The network address for the subnet and the original network is identical – Subnet Zero
Broadcast address for this subnet is 192.168.255.255, broadcast address for the original network is also 192.168.255.255 – All-One Subnet
We normally avoid “all zero” and “all one” subnets.

## Slide 31: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19

## Slide 32: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts

## Slide 33: CIDR Example
Address space – 203.110.0.0/19
  13 bits are available to serve all the hosts of IITKGP network
  We need to divide these address space among 3 subnets
CSE – 11 bits, VGSOM – 9 bits, EE – 9 bits for host address
We have 2 bits left for identifying three subnets – Is this possible?
  Avoid “all zero” and ”all one” subnets
Let us apply CIDR – Combine VGSOM and EE Networks together

## Slide 34: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts
10 bit hosts

## Slide 35: CIDR Example
CSE – 11 bits, VGSOM+EE – 10 bits
Network address – 203.110.0.0/19, 203.110.000XXXXX.XXXXXXXX
CSE network address 203.110.00010XXX.XXXXXXXX (203.110.16.0/21)
VGSOM+EE network address 203.110.00001XXX.XXXXXXXX (203.110.8.0/21)

## Slide 36: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts
10 bit hosts
203.110.16.0/21
203.110.8.0/21

## Slide 37: CIDR Example
VGSOM – 9 bits, EE – 9 bits
Network address – 203.110.8.0/21, 203.110.00001XXX.XXXXXXXX
VGSOM network address 203.110.0000110X.XXXXXXXX (203.110.12.0/23)
EE network address 203.110.0000101X.XXXXXXXX (203.110.10.0/23)

## Slide 38: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts
10 bit hosts
203.110.16.0/21
203.110.8.0/21
203.110.12.0/23
203.110.10.0/23

## Slide 39: CIDR – Routing Table Construction
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
Network | Netmask | Gateway | Interface
10.0.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.3.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.4.0 | 255.255.255.0 | 172.16.2.2 | eth1
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Routing Table for R1

## Slide 40: CIDR – Routing Table Construction
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
Network | Netmask | Gateway | Interface
10.0.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.3.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.4.0 | 255.255.255.0 | 172.16.2.2 | eth1
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Routing Table for R1
Compaction of routing table is possible

## Slide 41: CIDR – Routing Table Construction
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
Network | Netmask | Gateway | Interface
10.0.0.0 | 255.255.0.0 | 172.16.2.2 | eth1
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Compact
Routing Table for R1

## Slide 42: CIDR – Problem of Multihoming
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
eth2
172.16.3.1/24
172.16.3.2/24
10.0.4.2/24

## Slide 43: CIDR – Longest Prefix Match
Network | Netmask | Gateway | Interface
10.0.0.0 | 255.255.0.0 | 172.16.2.2 | eth1
10.0.5.0 | 255.255.255.0 | 172.16.3.2 | eth2
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Supernetting is not always perfect !
There is always a possibility of duplicate entries
Where to forward 10.0.5.8 ?

## Slide 44: CIDR – Longest Prefix Match
Use Patricia Tree (a compact representation of trie) for matching prefixes.
0
1
00
10
11
100
101
00*
0*
11*

## Slide 45: Next, we’ll look how to construct the routing table for the Internet …