## Slide 1: CS 31006: Computer Networks – The Routers

## Slide 2: The Life of a Router
Do
  Find Path
  Forward, forward, forward, forward, forward
  Find Path
  Forward, forward, forward, forward, forward
Repeat until powered off
Two basic operations –
  Construct the routing table – the control plane
  Do a routing match and forward the packet to a dedicated interface – the data plane

## Slide 3: Evolution of Router Architecture
1st Generation (Until 1980’s): Standard Computer
2nd Generation (Early 1990’s): Delegate to interfaces
3rd Generation (Late 1990’s): Distributed Architecture
4th Generation (Early 2000’s): Distributed over multiple racks
5th Generation (Today): Software Defined Routing

## Slide 4: Basic Architectural Components of a Router
Processor
Memory
CPU
Interconnection Network
Interface card
Interface card
Interface card
Interface card

## Slide 5: Router Hardware
Processor is responsible for control functions (route processors)
  Construct the routing table based on the routing algorithm
Forwarding is done at the interface card
  Route match needs to be very fast
  Specialized hardware – Ternary Content-Addressable Memory (TCAM)
Control Plane
Data Plane
Routing Table Construction
Forwarding

## Slide 6: Router Internals

## Slide 7: Slotted Chassis – The Physical Infrastructure for Routers
Large routers are built as slotted chassis
  Interface cards are inserted in the slots
  Route processor is also inserted at a slot
Simplifies repairs and upgrades of components

## Slide 8: Functional Components
Routing Functions
IP Forwarding
 | Routing Table | 
Table
Update
Route Lookup
Control
Datapath
Per Packet Processing

## Slide 9: Control Plane in a Router
Note that a router is a special purpose computer
Implemented as a software (router OS) that supports the basic computing functionalities to run a router along with routing functionalities
Routing protocols are implemented in the router OS
Example: Cisco IOS

## Slide 10: Routing Functions
Route Calculation
Maintenance of the routing table
Execution of the routing protocol
On commercial routers, routing functions are handled by a single general purpose processor, called the route processor

## Slide 11: Data Plane of a Router
Implement forwarding functionalities – make a route lookup and forward the packet at the destination interface
Functionality is similar to a L2 switch – use switch fabric (the mapping from input ports to output ports) to forward the packet from one interface to another
Maintains interface buffer – to implement store and forward functionality

## Slide 12: IP Forwarding
Per packet processing of the IP packets
IP forwarding is distributed, handled by individual interface controllers
Special hardware devices are used - TCAM

## Slide 13: Per Packet Processing – Basic Architectural Components
Routing Table

## Slide 14: Forwarding Information Base (FIB)
The interfaces maintains a forwarding information base (FIB) – a mapping from input interface to output interface
A replica of the routing table used at the interfaces for making the forwarding decision
FIB Lookup
Route Lookup
Forward Packet
Input Interface
Output
Interface
PACKET_IN
PACKET_OUT
Routing Protocols
FIB HIT
FIB MISS

## Slide 15: Difference between RIB and FIB
Routing Information Base (RIB) – The routing table, implemented in software, is maintained at the control plane
Forwarding Information Base (FIB) – The copy of the required routes maintained in interface TCAM hardware
RIB is dynamic and maintains entire routing information, FIB is updated whenever required

## Slide 16: RIB and FIB
172.16.1.0 | 255.255.255.0 | 172.16.1.2 | Eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | Eth1
10.3.0.0 | 255.255.0.0 | 10.3.1.1 | Eth3
10.9.0.0 | 255.255.0.0 | 10.9.1.1 | Eth4
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | Eth1
10.3.0.0 | 255.255.0.0 | 10.3.1.1 | Eth3
10.9.0.0 | 255.255.0.0 | 10.9.1.1 | Eth4
172.16.1.0 | 255.255.255.0 | 172.16.1.2 | Eth0
10.3.0.0 | 255.255.0.0 | 10.3.1.1 | Eth3
The RIB
FIB at Eth0
FIB at Eth1

## Slide 17: RIB Feeds FIB
Image source: Cisco

## Slide 18: Basic TCAM Architecture
Image Source: http://thenetworksherpa.com/

## Slide 19: A Demo of a Router Architecture

## Slide 20
Software Defined Networking
Software-defined networking (SDN) is a network framework which involves in separating a network's control functions from its data forwarding functions, centralizing its intelligence, and abstracting its underlying architecture from applications and services.
Indian Institute of Technology Kharagpur

## Slide 21
Control and Data Plane
Indian Institute of Technology Kharagpur
Control plane
  The module which takes all decisions, basically an instructor
  The routing algorithm
Data plane
  The module which carries out the tasks given by the control plane
  Forwarding of Packets

## Slide 22
Control and Data Plane
Indian Institute of Technology Kharagpur
Traditional networking devices are proprietary
  Vendors decide software (control plane) and hardware (data plane)
No standardization
These two modules are “baked” in
Unchangeable

## Slide 23
What does separating control and data plane mean?
Indian Institute of Technology Kharagpur
Vendors only provide the hardware (data plane)
We decide the control plane by writing custom logic – the software
But what if they were separate?

## Slide 24
What does separating control and data plane mean?
Indian Institute of Technology Kharagpur
Vendors only provide the hardware (data plane)
We decide the control plane by writing custom logic
Advantages:
Features are no longer limited to what the vendor provides
Community development
Longer life of products
But what if they were separate?

## Slide 25
How Does SDN Work
Indian Institute of Technology Kharagpur
Compared to traditional networks, a software defined network has 2 types of devices
  Controller
  Switches
The switches in SDN are blind
  No built-in features
  Need to be instructed by the controller
Zodiac FX - A Tiny SDN Switch

## Slide 26
h1
h3
s1
c0
SDN Controller
“Brains” of the network
All policies, routing logic are placed in the controller
“Teaches” the switches what to do with an unknown packet

## Slide 27
h1
h3
s1
c0
SDN Controller
“Brains” of the network
All policies, routing logic are placed in the controller
“Teaches” the switches what to do with an unknown packet
Let us now see a scenario where a packet wants to go from h1 to h3 in an SDN environment

## Slide 28
Forwarding Request from h1 to s1
h1
h3
s1
c0
SRC - h1
DST - h3

## Slide 29
?
Table MISS
Table Miss at s1
h1
h3
s1
c0
No rule is there for h1->h2 at the beginning, so a FIB miss at S1

## Slide 30
Till then, the packet is buffered at s1
Packet-IN
Packet-OUT
Packet-IN to Controller
h1
h3
s1
c0
?
Table MISS
The controller generates the rule based on a software program (the routing logic)

## Slide 31
Flow Rule Set at s1…
h1
h3
s1
c0
Rule 1
The rule is installed at the FIB of S1

## Slide 32
All Future Packets from h1->h3
h1
h3
s1
c0
Rule 1
The buffered packet is forwarded based on that rule

## Slide 33
Buffered Packet Forwarded to h3…
h1
h3
s1
c0
Rule 1
All the future packets from h1->h2 follow the same rule

## Slide 34: The SDN Architecture
Image source: qmonnet.github.io

## Slide 35: Tranditional Network vs SDN
Image source: http://opensourceforu.com/